## Slide 1: Sleepless in Seattle No Longer
Joshua Reich, Michel Goraczko, Aman Kansal, Jitendra Padhye
Columbia University & Micrsoft Research
Presented by Nishad Gothoskar

## Slide 2: Problem
  Desktop computers
    Laptops (usually)
      Awake  In Use
      Not In Use  Asleep
  Not the case with Desktops
    Users want them to always be accessible
    Because they aren’t mobile
  Enterprise networks (office building) may have hundreds to thousands of these machines
    Only actually being used for a fraction of the time they are actually awake (remaining time  energy waste)
    2/3 are left on all the time

## Slide 3: Problem
  Dilemma: If I Sleep I may “Miss Something”
    Once you sleep you have no network presence
  But there’s a high chance you won’t miss anything
  Enterprises aren’t willing to take that chance
    Remote access
    IT (updates, security)
  Issue similar to what we saw in Networking Energy
  You don’t know when or if an event will occur
  so you wait...

## Slide 4: Solution
  Why should every computer be in the “wait” state?
  “wait” isn’t very processor intensive but still keeps the computer hardware running (consumes power)
  SleepServer
  Why not let one system manage all the computers “wait” states and let them sleep?
  Sleep Proxy

## Slide 5: Inspiration
  Many ideas from Somniloquy and SleepServer
  But what’s different?
    The question with SleepServer was what do we want to virtualize
      Entire VM (too much)
  SleepProxy – monitors network traffic and allows us to maintain network presence even while asleep
  Paper cites Somniloquy and SleepServer

## Slide 6: Vocabulary
  ARP – address resolution protocol
    Map between network and hardware addresses
    ARP Probes – used to reroute incoming packets
  NIC – network interface controller
  WOL – Wake-on-LAN (who will send the signal?)
  TCP SYN – opening a connection

## Slide 7: Architecture