## Slide 1: Reducing network energy consumption via sleeping and rate-adaptation
Nedevschi, Popa, Iannaccone, Ratnasamy, Wetherall
UC Berkeley, Intel Research, U of Washington
Presented by Nishad Gothoskar

## Slide 2: Problem
  Network Energy Consumption
    Device
    Router
  Reoccurring themes
    Utilization is low < 30%
    Devices are built for worst case (peak)
    High consumption even in idle state
  We see this issues with
    Processors, Mobile Devices, Mobile Networks
    Energy dis-proportionality

## Slide 3: Problem
  Backbone of the Internet
    Essential infrastructure
  Networks are growing and expanding
  Speed demands are increasing
  Networks will become extremely power hungry
  But, Energy costs and Environment concerns
  Need to find a way to Energy optimize networks

## Slide 4: Solution
Sleep
States
Performance
States
Somniloquy
SleepServer SleepProxy
(Computers)
DVFS
(Computers)
ACPI
(Computers)

## Slide 5: Solution
Sleep
States
Performance
States
Find state
ps
With
pi > ps
Reduce
pa and pi
and increase
Ta
E=paTa + piTi

## Slide 6: Method
  Assume certain network hardware exists
    With these dynamic states
      Sleep
      Performance
  Very different from our previous papers
  Use models / simulations of networks
  Write algorithms
  Analyze and evaluate how this network hardware would improve energy usage in that model
  * Criticism *

## Slide 7: Models
  Record the network traces
  ns2 – packet-level simulator
  Intel and Abilene
  Router Netflow records per minute
  Very realistically be able to model with precision the network traffic and information flow

## Slide 8: Sleep
  Benefit comes from psleep
  Must consider δ which is the transition period
  Takes advantage of timer-driven sleep to coordinate a buffer interval of Bms

## Slide 9: Sleep (2)
  Called the Buffer and Burst strategy
  Many times the delay is the downside
    This strategy ensures upper bound of B
  Developed two algorithms
    Optimal B&B
      Perfectly coordinated
      Forgets delta
    Practical B&B
      Takes into account delta
      More realistic and alike to something we could implement

## Slide 10: Data

## Slide 11: Data

## Slide 12: Data

## Slide 13: Data Analysis
  Savings vs. performance
  Balanced metric
  Savings – (sleep timeenergy) compare prac to opt
  Performance – (delay) compare prac to none
    Drop bits
  Usefulness highly dependent on parameters
  In general, low utilization and B=5ms  60% sleep
  Delta is essential  design hardware with low delta

## Slide 14: Rate Adaption
  Different performance rates r1, r2, r3, r4…
  Must consider δ which is the transition period
r1,

## Slide 15: Rate Adaption
  Optimization problem
  Because Energy ~ Transmission rate
r1,

## Slide 16: Rate Adaption (2)
  The practical algorithm
    Takes discrete values
    Online
  Same data analysis as previous part involving the Savings vs. Performance between prac and opt

## Slide 17: Data

## Slide 18: Data

## Slide 19: Results
  Results are dependent on the power consumption in each of the states and the ratios between them

## Slide 20: Conclusion
  Lets address the big problem
  NO implementation ALL simulations
  This research provides the basis of how to develop new network hardware